## Slide 1: ASIC design: approach 1
01/08/2021

## Slide 2: AES algorithm’s steps

## Slide 3
Substitution according to table
Shifting
Multiplication matrix x matrix
XOR between matrix (3) and round key
  Upwards shift
  Substitution (step 1)
  XOR between matrix column and corresponding rc constant
Key
Generation

## Slide 4
AXI 4 (bus)
ROM
(Rijndael
S-box)
Key Gen.
Encoding
ROM
(rc cons)
Keyi storage
(4x4 matrix)
XOR
(16 blocks)
Shifters
(16 sfts, 4 blks of 4-serial sfts)
Subs
(16 blocks)
Subs
(16 blocks)
Shifters
(16 sfts, 4 blks of 4-serial shts)
AddRoundKey (XOR)
(16 blocks)
Multipl.
(16 muls, 4 sums)
Galinois’ check
(…)
Comp_mul_2to1.sv
Notes: NOTE: Maybe the “Upward shift” step is only performed with the first column and we only perform and XOR with the rest of the key’s column (check https://towardsdatascience.com/aes-encryption-256-bit-a9ae49cde0b6 for more details).

## Slide 5: Extra notes
The ASIC schematic is divided into two parts since the key generation process and the encryption of the data can be done in parallel.
Since the shifters are used simultaneously and in different directions (sidewards vs upwards), I decided to implement two modules
Problem: Galinois’ multiplication
Further investigation should be carried in order to merge the data extracted from the AES’ code and the gates/schematic that will be implemented in the ASIC.

## Slide 6: List of components
Encryption side (enc) | .sv done | tb | Use of matrices
Subsitution (module) | progress | - | 
Shifter (module) | OK | OK | OK
MixColumns (module) | - | - | 
Multiplicator (module) | OK | - | 
Multiplicator (component) | OK | - | 
Adder (component) | OK | - | 
Galois operator (module) | - | - | 
AddRoundKey (module) | OK | OK | OK
ROM |  |  | 
Keygen side (keygen) | .sv done | tb | Use of matrices
Shifter (module) | OK | Done but not working | OK
Substitution (module) | progress | - | 
XOR (module) | - | - | 
Overall | .sv done | tb | Use of matrices
Device | - | - | 
reg16 | OK | OK | OK

## Slide 7: 16-bit register
Notes: Creating a ROM verilog:
https://vlsiworld-asic.blogspot.com/2012/02/verilog-code-for-ram-rom.html
https://github.com/Obijuan/open-fpga-verilog-tutorial/wiki/Cap%C3%ADtulo-26:-Memoria-ROM

## Slide 8: tb: successful

## Slide 9: Substitution (module, enc & keygen)
Notes: Creating a ROM verilog:
https://vlsiworld-asic.blogspot.com/2012/02/verilog-code-for-ram-rom.html
https://github.com/Obijuan/open-fpga-verilog-tutorial/wiki/Cap%C3%ADtulo-26:-Memoria-ROM

## Slide 10: tb: SUCCESSFUL

## Slide 11: Shifter (enc)

## Slide 12: tb: SUCCESSFUL
p00 | 00 | o00 | 00
p01 | 01 | o01 | 01
p02 | 02 | o02 | 02
p03 | 03 | o03 | 03
p10 | 04 | o10 | 05
p11 | 05 | o11 | 06
p12 | 06 | o12 | 07
p13 | 07 | o13 | 04
p20 | 08 | o20 | 10
p21 | 09 | o21 | 11
p22 | 10 | o22 | 08
p23 | 11 | o23 | 09
p30 | 12 | o30 | 15
p31 | 13 | o31 | 12
p32 | 14 | o32 | 13
p33 | 15 | o33 | 14

## Slide 13: Multiplicator (submodule, enc)
8-bit number
8-bit number
Comp_mul_2to1.sv
16-bit number
8-bit number
8-bit number
16-bit number
8-bit number
8-bit number
16-bit number
8-bit number
8-bit number
16-bit number
16-bit number
Comp_sum_4to1.sv
C
8
8
8
8
8
8
8
8
16-bit number

## Slide 14: Multiplicator (module, enc)
8-bit
8-bit
16-bit
8-bit
8-bit
16-bit
8-bit
8-bit
16-bit
8-bit
8-bit
16-bit
16-bit
C
8
8
8
8
8
8
8
8
16-bit
…
1
2
16
P00 (16-bit)
P01 (16-bit)
P33 (16-bit)

## Slide 15: tb:

## Slide 16: AddRoundKey (enc)
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
8
8
8
8
8
8
8
8
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
8
8
8
8
8
8
8
8
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
8
8
8
8
8
8
8
8
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
8
8
8
8
8
8
8
8
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
8-bit
Notes: Doubt 1: The output for the XOR modules, having an input of two 8-bit numbers, will be 8-bit or 16-bit?

## Slide 17: tb: SUCCESSFUL
Position | Pxy hex (dec) | Kxy hex (dec) | oxy
00 | 00 (00) | 0A (10) | 0A
01 | 01 (01) | 0A (10) | 0B
02 | 02 (02) | 0A (10) | 08
03 | 03 (03) | 0A (10) | 09
10 | 0A (10) | 0F (15) | 05
11 | 0B (11) | 0F (15) | 04
12 | 0C (12) | 0F (15) | 03
13 | 0D (13) | 0F (15) | 02
20 | 14 (20) | 14 (20) | 00
21 | 15 (21) | 14 (20) | 01
22 | 16 (22) | 14 (20) | 02
23 | 17 (23) | 14 (20) | 03
30 | 1E (30) | 28 (40) | 36
31 | 1F (31) | 28 (40) | 37
32 | 20 (32) | 28 (40) | 08
33 | 21 (33) | 28 (40) | 09
Notes: Website for manual verification: https://xor.pw/#
Hexadecimal to decimal conversion and vice versa: https://www.rapidtables.com/convert/number/hex-to-decimal.html

## Slide 18
=
XOR

## Slide 19: Shifter (keygen)

## Slide 20: tb: SUCCESSFUL
p00 | 00 | o00 | 01
p01 | 01 | o01 | 02
p02 | 02 | o02 | 03
p03 | 03 | o03 | 00